## Slide 1: Lead-Acid Battery Charger
Gajaanan S. -190185D
Pankajan T. -190428D
luXshan S. -190364C
Mokeeshan V.-190395V

## Slide 2: Overview
Introduction
Circuit Explanation
Project timeline
Progress
References

## Slide 3: Battery charging…
Specifications-
  230V AC to 30V DC converter and regulator
  8A current
  CCCV method
Introduction
Progress
Circuit
Timeline
References

## Slide 4: Functional Block Diagram
PWM Waveform Generation
Smoothing Circuit
Obtain30V DC Voltage
Generate Triangular waveform
24V, 8A Lead Acid Battery
230V AC Source
V<Vref(28.8V)
Constant current mode
Constant voltage mode
Adjust PWM based on current(A) reading.
Adjust PWM based on voltage across battery.
Yes
No
Switching Circuit
Introduction
Progress
Circuit
Timeline
References

## Slide 5
Introduction
Progress
Circuit
Timeline
References
1st Week
Finalize circuit and Components
2nd Week
Start to build Circuit physically
4th Week
Print PCB and finish
Finalize physical circuit
3rd Week

## Slide 6: PWM generation-Method 1
Triangular wave Generator- U1A & U2A op-amp circuits.
  , ,
  Voltage across C2 oscillate in between and .
Comparator- U1C op-amp circuit
  Triangular wave compares the voltage with Vin and produces PWM waveform.
  Input voltage(V1) for U1c decides the duty cycle of PWM.
Introduction
Progress
Circuit
Timeline
References

## Slide 7: PWM generation-Method 2
Introduction
Progress
Circuit
Timeline
References
Astable vibrator
Comparator
    Here also input voltage(V2) for U2A decides the duty cycle of PWM.
Adder circuit
    amplification and remove the negative part

## Slide 8: Smoothing Circuit
Introduction
Progress
Circuit
Timeline
References
Buck converter had been selected to smooth the PWM waveform and to convert voltage(DC to DC)
Change the output regarding the duty cycle of PWM.

## Slide 9: Switching-Method 1
1) Comparator
If Battery voltage < 28.8 V, Comparator will produce 0V.
If Battery voltage > 28.8 V, Comparator will produce 5V.
2) 5V relay
If Comparator output voltage = 0V ,
  Initially, the relay will connect a constant current mode connection.
If Comparator output voltage = 5V ,
  The relay will connect a constant voltage mode connection.
Introduction
Progress
Circuit
Timeline
References

## Slide 10: Switching-Method 2
Using Power MOSFETs to control the constant current and constant voltage part.
If Battery voltage > 28.8 V,
  Comparator will produce 10V. So, Inially, N-MOSFET will connect constant current mode connection.
If Battery voltage < 28.8 V,
  Comparator will produce -10V. So, P-MOSFET will connect constant current mode connection
Introduction
Progress
Circuit
Timeline
References

## Slide 11: Constant Current Control
Approach:
  Measure the current
  find out the error
  manipulate the PWM signal
Low-side current sensing for current measurement
  We chose low-side current measurement for a cost-effective solution and easy implementation.
  This low-side current sensing has an operational amplifier in a non-inverting configuration.
Differential amplifier circuit for error measurement
  A differential amplifier is used to measure error.
  Stationary voltage previously calculated should be applied since it corresponds to 8A
Introduction
Progress
Circuit
Timeline
References

## Slide 12
INTEGRATOR CIRCUIT FOR ADJUSTING PWM SIGNAL
Error value is applied to the integrator circuit to adjusting the PWM signals.
𝑉𝑂𝑈𝑇(𝑃𝑊𝑀 𝑐𝑜𝑛𝑡𝑟𝑜𝑙) = − 𝑑𝑡 = − 𝑑𝑡
If 8A > ILOAD ,
  Vout maintains increasing until the correct voltage is wanted for the PWM duty cycle.
If 8A < ILOAD ,
  Vout maintains decreasing until the correct voltage is wanted for the PWM duty cycle.
Introduction
Progress
Circuit
Timeline
References

## Slide 13: Constant Voltage Control
Approach:
  Measure the voltage across battery
  find out the error
  integrating circuit (Possibly the entire PID system)
Voltage of the battery is divided then read through differential amplifier
Then the output is again sent to a differential amplifier for error calculation => if Vout<0: Vsupply increases Vout>0: Vsupply decreases
Introduction
Progress
Circuit
Timeline
References

## Slide 14
Lastly, the error value will be sent to an integrator circuit. t; accumulation of error values
Consideration of PID instead of just integrator. By using this system, we could reduce the oscillation overshooting and achieve result faster.
Introduction
Progress
Circuit
Timeline
References

## Slide 15: Some other circuit findings
Introduction
Progress
Circuit
Timeline
References

## Slide 16: AC-DC converter
Introduction
Progress
Circuit
Timeline
References

## Slide 17: Up to now….
Find various battery charging methods and theories behind circuits.
Finished calculations for PWM based circuit
Have working simulations for PWM.
Build the basic physical circuit on breadboard for PWM,CC and CV
Introduction
Progress
Circuit
Timeline
References

## Slide 18
https://www.ti.com/lit/an/sboa169b/sboa169b.pdf?ts=1647110122143
https://eeebooks4u.com/2021/05/29/astable-multivibrator-using-op-amp/
https://batteryuniversity.com/article/bu-403%20charging-lead-acid
https://www.hilarispublisher.com/open-access/charging-leadacid-batteries.pdf
https://www.engineeringenotes.com/electrical-engineering/batteries/charging-of-lead-acid-battery-methods-and-precaution-electricity/29991
Introduction
Progress
Circuit
Timeline
References

## Slide 19: Thank you